## Slide 2
Founded in 1910 starting with waterproofing of tunnels in Europe
Subsidiaries in 100 countries with sales > $7 billion
Over 17,000 employees with focus on innovation, about 1,000 people in R&D
Leader in concrete expertise and concrete repair & protection products
Still growing with a floor to roof construction product offering
Sika global experience

## Slide 3: Sika’s target markets
Flooring
Concrete Products
Roofing
Waterproofing
Residential
Repair & Protection
Sealants & Adhesives
Industry/Manufacturing
Automotive/Transportation

## Slide 4: Sealants

## Slide 5: Joint Design and Installation
Match joint size to sealant movement capability - best 4 times anticipated
2:1 width to depth ratio is best
Install backer rod or tape to prevent 3-sided adhesion and control depth
Best to do work when joint at midpoint of movement
Sealant needs to be tooled to force it against the joint walls

## Slide 6: Astm C-920 Sealant specification
Type: S or M
  Single or Multi-component
Grade: P or NS
  Pourable or Non-Sag
Class: 12.5, 25, 50, 100/50
  % of movement
Use: T, NT, I, M, G, A, O
  Traffic
  Non-traffic
  Immersion
  Mortar
  Glass
  Aluminum
  Other

## Slide 7: Sikaflex 1a and Sikaflex 1cSL

## Slide 8: Sikaflex 15 LM and Sika Hybrid 150 LM
Sikaflex 15 LM
Vertical
Most movement
EIFS
Sika Hybrid 150 LM
Hybrid sealant
White stays white
Better bond to vinyl

## Slide 9: Sikaflex 2c NS/SL
Two component urethane sealants
1.5 gallon and 3 gallon pails

## Slide 10: Sikaflex 11 FC
Elastomeric adhesive
Fast cure
Equivalent to Liquid Nails

## Slide 11: Sikasil 295 and Sikasil 290
Silicone sealants
Bonding to glass
Longest life expectancy
Non Staining
295 equal to Dow 795,756, Pecora 895, 864, Spectrum 2,3, SCS2000, and SCS 9000.

## Slide 12: Sikasil GP
Bathrooms
Kitchens

## Slide 13: Sealant Innovations
Sikaflex 2c NS Arctic
Two-component, non-sag, polyurethane sealant
Cold temperature mix and apply down to 15F.
For installations when temperatures are between 15F and 50F. For 50F and over use standard EZ Mix formula.

## Slide 14: SEALANTS

## Slide 15: SEALANTS

## Slide 16: SEALANTS

## Slide 17: SEALANTS

## Slide 18: SEALANTS